## Slide 1: Module 2: Single-Area OSPFv2 Configuration
Instructor Materials
Enterprise Networking, Security, and Automation v7.0
(ENSA)
Notes: Cisco Networking Academy Program
Enterprise Networking, Security, and Automationv7.0 (ENSA)
Module 2: Single-Area OSPFv2 Configuration

## Slide 2: Instructor Materials – Module 2 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the module
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 13
  Note: Remove the Planning Guide from this presentation before sharing with anyone.
For additional help and resources go to the Instructor Home Page and Course Resources for this course. You also can visit the professional development site on netacad.com, the official Cisco Networking Academy Facebook page, or Instructor Only FB group.
Notes: 2

## Slide 3: What to Expect in this Module
To facilitate learning, the following features within the GUI may be included in this module:
Feature | Description
Animations | Expose learners to new skills and concepts.
Videos | Expose learners to new skills and concepts.
Check Your Understanding(CYU) | Per topic online quiz to help learners gauge content understanding.
Interactive Activities | A variety of formats to help learners gauge content understanding.
Syntax Checker | Small simulations that expose learners to Cisco command line to practice configuration skills.
PT Activity | Simulation and modeling activities designed to explore, acquire, reinforce, and expand skills.

## Slide 4: What to Expect in this Module (Cont.)
To facilitate learning, the following features may be included in this module:

## Slide 5: Check Your Understanding
Check Your Understanding activities are designed to let students quickly determine if they understand the content and can proceed, or if they need to review.
Check Your Understanding activities do not affect student grades.
There are no separate slides for these activities in the PPT. They are listed in the notes area of the slide that appears before these activities.
Notes: 5

## Slide 6: Packet Tracer Physical Mode Activities
These activities are completed using Packet Tracer in Physical Mode.
They are designed to emulate the corresponding Labs.
They can be used instead of the lab when access to physical equipment is not possible.
Packet Tracer Physical Mode activities may not have as much scaffolding as the PT activities that immediately precede them.
Notes: 6

## Slide 7: Module 2: Activities
What activities are associated with this module?
Page # | Activity Type | Activity Name | Optional?
2.1.8 | Syntax Checker | Configure R2 and R3 Router IDs | Recommended
2.1.9 | Check Your Understanding | OSPF Router ID | Recommended
2.2.3 | Check Your Understanding | The Wildcard Mask | Recommended
2.2.5 | Syntax Checker | Configure R2 and R3 Using the network Command | Recommended
2.2.7 | Syntax Checker | Configure R2 and R3 Using the ip ospf Command | Recommended
2.2.10 | Syntax Checker | Configure R2 and R3 Passive Interfaces | Recommended
2.2.13 | Packet Tracer | Point-to-Point Single-Area OSPFv2 Configuration | Recommended
2.3.10 | Syntax Checker | Configure OSPF Priority | Recommended
Notes: 7

## Slide 8: Module 2: Activities (Cont.)
What activities are associated with this module?
Page # | Activity Type | Activity Name | Optional?
2.3.11 | Packet Tracer | Determine the DR and BDR | Recommended
2.4.6 | Syntax Checker | Modify the Cost Values for R2 and R3 | Recommended
2.4.10 | Syntax Checker | Modifying Hello and Dead Intervals on R3 | Recommended
2.4.11 | Packet Tracer | Modify Single-Area OSPFv2 | Recommended
2.5.3 | Packet Tracer | Propagate a Default Route in OSPFv2 | Recommended
2.6.5 | Syntax Checker | Verify Single-Area OSPFv2 Configuration | Recommended
2.6.6 | Packet Tracer | Verify Single-Area OSPFv2 Configuration | Recommended
Notes: 8

## Slide 9: Module 2: Activities (Cont.)
What activities are associated with this module?
Page # | Activity Type | Activity Name | Optional?
2.7.1 | Packet Tracer | Single-Area OSPFv2 Configuration | Recommended
2.7.2 | Packet Tracer Physical Mode | Single-Area OSPFv2 Configuration | Recommended
2.7.2 | Lab | Single-Area OSPFv2 Configuration | Recommended
2.7.3 | Packet Tracer Physical Mode | Multi-Area OSPF Scenario | Recommended
2.7.5 | Module Quiz | Single-Area OSPFv2 Configuration | Recommended
Notes: 9

## Slide 10: Module 2: Best Practices
Prior to teaching Module 2, the instructor should:
Review the activities and assessments for this module.
Try to include as many questions as possible to keep students engaged during classroom presentation.
After this Module, the OSPF Concepts and Configuration Exam is available, covering Modules 1-2.
Topic 2.1
  Ask the students or have a class discussion
    What is the importance of the Router ID for OSPF?
    Discus additional examples of the Router-ID selection process and priorities
Notes: 10

## Slide 11: Module 2: Best Practices (Cont.)
Topic 2.2
  Ask the students or have a class discussion
    Discuss the pros and cons of the two different methods of including an interface in OSPF.
    Use examples where the passive-interface command is incorrectly employed to emphasize its purpose.
Topic 2.3
  Ask the students or have a class discussion
    Provide additional example scenarios of DR elections to ensure students understand the process thoroughly.
    What method would you use to ensure the “right” device is elected DR? What qualifies the device as “right”?
Topic 2.4
  Ask the students or have a class discussion
    Illustrate situations where the hello timers might be changed to influence network convergence speed or stability.
    Use the reference topology (or another topology) and illustrate cost accumulation in an OSPF network.
Notes: 11

## Slide 12: Module 2: Best Practices (Cont.)
Topic 2.5
  Ask the students or have a class discussion
    Instead of using a propagated default route, why wouldn’t you simply use static default routes on all the internal routers?
    What do you notice about the cost of a default route that has been propagated through OSPF?
Topic 2.6
  Ask the students or have a class discussion
    What command would you use to display a snapshot of your OSPF neighbor status?
    What command would you use to display details about the SPF algorithm’s operations?
Notes: 12

## Slide 13: Module 2: Single-Area OSPFv2 Configuration
Enterprise Networking, Security, and Automation v7.0
(ENSA)
Notes: Cisco Networking Academy Program
Enterprise Networking, Security, and Automationv7.0 (ENSA)
Module 2: Single-Area OSPFv2 Configuration

## Slide 14: Module Objectives
Module Title: Single-Area OSPFv2 Configuration
Module Objective: Implement single-area OSPFv2 in both point-to-point and broadcast multiaccess networks.
Topic Title | Topic Objective
OSPF Router ID | Configure an OSPFv2 router ID.
Point-to-Point OSPF Networks | Configure single-area OSPFv2 in a point-to-point network.
Multiaccess OSPF Networks | Configure the OSPF interface priority to influence the DR/BDR election in a multiaccess network.
Modify Single-Area OSPFv2 | Implement modifications to change the operation of single-area OSPFv2.
Default Route Propagation | Configure OSPF to propagate a default route.
Verify Single-Area OSPFv2 | Verify a single-area OSPFv2 implementation.
Notes: 14
2.0 – Introduction
2.0.2 – What will I learn to do in this module?

## Slide 15: 2.1 OSPF Router ID
Notes: 2 - Single-Area OSPFv2 Configuration
2.1 - OSPF Router ID

## Slide 16: OSPF Router ID OSPF Reference Topology
The figure shows the topology used for configuring OSPFv2 in this module. The routers in the topology have a starting configuration, including interface addresses. There is currently no static routing or dynamic routing configured on any of the routers. All interfaces on R1, R2, and R3 (except the loopback 1 on R2) are within the OSPF backbone area. The ISP router is used as the gateway to the internet of the routing domain.
Notes: 2 - Single-Area OSPFv2 Configuration
2.1 - OSPF Router ID
2.1.1 - OSPF Reference Topology

## Slide 17: OSPF Router ID Router Configuration Mode for OSPF
OSPFv2 is enabled using the router ospf process-id global configuration mode command. The process-id value represents a number between 1 and 65,535 and is selected by the network administrator. The process-id value is locally significant. It is considered best practice to use the same process-id on all OSPF routers.
R1(config)# router ospf 10
R1(config-router)# ?
area OSPF area parameters
auto-cost Calculate OSPF interface cost according to bandwidth
default-information Control distribution of default information
distance Define an administrative distance
exit Exit from routing protocol configuration mode
log-adjacency-changes Log changes in adjacency state
neighbor Specify a neighbor router
network Enable routing on an IP network
no Negate a command or set its defaults
passive-interface Suppress routing updates on an interface
redistribute Redistribute information from another routing protocol
router-id router-id for this OSPF process
R1(config-router)#
Notes: 2 - Single-Area OSPFv2 Configuration
2.1 - OSPF Router ID
2.1.2 - Router Configuration Mode for OSPF

## Slide 18: OSPF Router ID Router IDs
An OSPF router ID is a 32-bit value, represented as an IPv4 address. It is used to uniquely identify an OSPF router, and all OSPF packets include the router ID of the originating router.
Every router requires a router ID to participate in an OSPF domain. It can be defined by an administrator or automatically assigned by the router. The router ID is used by an OSPF-enabled router to do the following:
  Participate in the synchronization of OSPF databases – During the Exchange State, the router with the highest router ID will send their database descriptor (DBD) packets first.
  Participate in the election of the designated router (DR) - In a multiaccess LAN environment, the router with the highest router ID is elected the DR. The routing device with the second highest router ID is elected the backup designated router (BDR).
Notes: 2 - Single-Area OSPFv2 Configuration
2.1 - OSPF Router ID
2.1.3 - Router IDs

## Slide 19: OSPF Router ID Router ID Order of Precedence
Cisco routers derive the router ID based on one of three criteria, in the following preferential order:
The router ID is explicitly configured using the OSPF router-id rid router configuration mode command. This is the recommended method to assign a router ID.
The router chooses the highest IPv4 address of any of configured loopback interfaces.
The router chooses the highest active IPv4 address of any of its physical interfaces.
Notes: 2 - Single-Area OSPFv2 Configuration
2.1 - OSPF Router ID
2.1.4 - Router ID Order of Precedence

## Slide 20: OSPF Router ID Configure a Loopback Interface as the Router ID
Instead of relying on physical interface, the router ID can be assigned to a loopback interface. Typically, the IPv4 address for this type of loopback interface should be configured using a 32-bit subnet mask (255.255.255.255). This effectively creates a host route. A 32-bit host route would not get advertised as a route to other OSPF routers.
OSPF does not need to be enabled on an interface for that interface to be chosen as the router ID.
Notes: 2 - Single-Area OSPFv2 Configuration
2.1 - OSPF Router ID
2.1.5 – Configure a Loopback Interface as the Router ID

## Slide 21: OSPF Router ID Explicitly Configure a Router ID
In our reference topology the router ID for each router is assigned as follows:
R1 uses router ID 1.1.1.1
R2 uses router ID 2.2.2.2
R3 uses router ID 3.3.3.3
Use the router-id rid router configuration mode command to manually assign a router ID. In the example, the router ID 1.1.1.1 is assigned to R1. Use the show ip protocols command to verify the router ID.
R1(config)# router ospf 10
R1(config-router)# router-id 1.1.1.1
R1(config-router)# end
*May 23 19:33:42.689: %SYS-5-CONFIG_I: Configured from console by console
R1# show ip protocols | include Router ID
Router ID 1.1.1.1
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.1 - OSPF Router ID
2.1.5 - Configure a Loopback Interface as the Router ID

## Slide 22: OSPF Router ID Modify a Router ID
After a router selects a router ID, an active OSPF router does not allow the router ID to be changed until the router is reloaded or the OSPF process is reset.
Clearing the OSPF process is the preferred method to reset the router ID.
R1# show ip protocols | include Router ID
Router ID 10.10.1.1
R1# conf t
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# router ospf 10
R1(config-router)# router-id 1.1.1.1
% OSPF: Reload or use "clear ip ospf process" command, for this to take effect
R1(config-router)# end
R1# clear ip ospf process
Reset ALL OSPF processes? [no]: y
*Jun 6 01:09:46.975: %OSPF-5-ADJCHG: Process 10, Nbr 3.3.3.3 on GigabitEthernet0/0/1 from FULL to DOWN, Neighbor Down: Interface down or detached
*Jun 6 01:09:46.981: %OSPF-5-ADJCHG: Process 10, Nbr 3.3.3.3 on GigabitEthernet0/0/1 from LOADING to FULL, Loading Done *
R1# show ip protocols | include Router ID
Router ID 1.1.1.1
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.1 - OSPF Router ID
2.1.7 - Modify a Router ID
2.1.8 - Syntax Checker - Configure R2 and R3 Router IDs
2.1.9 - Check Your Understanding - OSPF Router ID

## Slide 23: 2.2 Point-to-Point OSPF Networks
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks

## Slide 24: Point-to-Point OSPF Networks The network Command Syntax
You can specify the interfaces that belong to a point-to-point network by configuring the network command. You can also configure OSPF directly on the interface with the ip ospf command.
The basic syntax for the network command is as follows:
Router(config-router)# network network-address wildcard-mask area area-id
The network-address wildcard-mask syntax is used to enable OSPF on interfaces. Any interfaces on a router that match this part of the command are enabled to send and receive OSPF packets.
The area area-id syntax refers to the OSPF area. When configuring single-area OSPFv2, the network command must be configured with the same area-id value on all routers. Although any area ID can be used, it is good practice to use an area ID of 0 with single-area OSPFv2. This convention makes it easier if the network is later altered to support multiarea OSPFv2.
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.1 - The network Command Syntax

## Slide 25: Point-to-Point OSPF Networks The Wildcard Mask
The wildcard mask is typically the inverse of the subnet mask configured on that interface.
The easiest method for calculating a wildcard mask is to subtract the network subnet mask from 255.255.255.255, as shown for /24 and /26 subnet masks in the figure.
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.2 - The Wildcard Mask
2.2.3 - Check Your Understanding - The Wildcard Mask

## Slide 26: Point-to-Point OSPF Networks Configure OSPF Using the network Command
Within routing configuration mode, there are two ways to identify the interfaces that will participate in the OSPFv2 routing process.
In the first example, the wildcard mask identifies the interface based on the network addresses. Any active interface that is configured with an IPv4 address belonging to that network will participate in the OSPFv2 routing process.
Note: Some IOS versions allow the subnet mask to be entered instead of the wildcard mask. The IOS then converts the subnet mask to the wildcard mask format.
R1(config)# router ospf 10
R1(config-router)# network 10.10.1.0 0.0.0.255 area 0
R1(config-router)# network 10.1.1.4 0.0.0.3 area 0
R1(config-router)# network 10.1.1.12 0.0.0.3 area 0
R1(config-router)#
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.4 - Configure OSPF Using the network Command

## Slide 27: Point-to-Point OSPF Networks Configure OSPF Using the network Command (Cont.)
As an alternative, OSPFv2 can be enabled by specifying the exact interface IPv4 address using a quad zero wildcard mask. Entering network 10.1.1.5 0.0.0.0 area 0 on R1 tells the router to enable interface Gigabit Ethernet 0/0/0 for the routing process.
The advantage of specifying the interface is that the wildcard mask calculation is not necessary. Notice that in all cases, the area argument specifies area 0.
R1(config)# router ospf 10
R1(config-router)# network 10.10.1.1 0.0.0.0 area 0
R1(config-router)# network 10.1.1.5 0.0.0.0 area 0
R1(config-router)# network 10.1.1.14 0.0.0.0 area 0
R1(config-router)#
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.4 - Configure OSPF Using the network Command (Cont.)
2.2.5 - Syntax Checker - Configure R2 and R3 using the network Command

## Slide 28: Point-to-Point OSPF Networks Configure OSPF Using the ip ospf Command
To configure OSPF directly on the interface, use the ip ospf interface configuration mode command. The syntax is as follows:
Router(config-if)# ip ospf process-id area area-id
Remove the network commands using the no form of the command. Then go to each interface and configure the ip ospf command
R1(config)# router ospf 10
R1(config-router)# no network 10.10.1.1 0.0.0.0 area 0
R1(config-router)# no network 10.1.1.5 0.0.0.0 area 0
R1(config-router)# no network 10.1.1.14 0.0.0.0 area 0
R1(config-router)# interface GigabitEthernet 0/0/0
R1(config-if)# ip ospf 10 area 0
R1(config-if)# interface GigabitEthernet 0/0/1
R1(config-if)# ip ospf 10 area 0
R1(config-if)# interface Loopback 0
R1(config-if)# ip ospf 10 area 0
R1(config-if)#
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.6 - Configure OSPF Using the ip ospf Command
2.2.7 - Syntax Checker - Configure R2 and R3 using the ip ospf Command

## Slide 29: Point-to-Point OSPF Networks Passive Interface
By default, OSPF messages are forwarded out all OSPF-enabled interfaces. However, these messages only need to be sent out interfaces that are connecting to other OSPF-enabled routers.
Sending out unneeded messages on a LAN affects the network in three ways:
Inefficient Use of Bandwidth - Available bandwidth is consumed transporting unnecessary messages.
Inefficient Use of Resources - All devices on the LAN must process and eventually discard the message.
Increased Security Risk - Without additional OSPF security configurations, OSPF messages can be intercepted with packet sniffing software. Routing updates can be modified and sent back to the router, corrupting the routing table with false metrics that misdirect traffic.
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.8 - Passive Interface

## Slide 30: Point-to-Point OSPF Networks Configure Passive Interfaces
Use the passive-interface router configuration mode command to prevent the transmission of routing messages through a router interface, but still allow that network to be advertised to other routers.
The show ip protocols command is then used to verify that the interface is listed as passive.
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.9 - Configure Passive Interfaces
2.2.10 - Syntax Checker - Configure R2 and R3 Passive Interfaces

## Slide 31: Point-to-Point OSPF Networks OSPF Point-to-Point Networks
By default, Cisco routers elect a DR and BDR on Ethernet interfaces, even if there is only one other device on the link. You can verify this with the show ip ospf interface command. The DR/ BDR election process is unnecessary as there can only be two routers on the point-to-point network between R1 and R2. Notice in the output that the router has designated the network type as BROADCAST.
R1# show ip ospf interface GigabitEthernet 0/0/0
GigabitEthernet0/0/0 is up, line protocol is up
Internet Address 10.1.1.5/30, Area 0, Attached via Interface Enable
Process ID 10, Router ID 1.1.1.1, Network Type BROADCAST, Cost: 1
Topology-MTID Cost Disabled Shutdown Topology Name
0 1 no no Base
Enabled by interface config, including secondary ip addresses
Transmit Delay is 1 sec, State BDR, Priority 1
Designated Router (ID) 2.2.2.2, Interface address 10.1.1.6
Backup Designated router (ID) 1.1.1.1, Interface address 10.1.1.5
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
oob-resync timeout 40
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.11 - OSPF Point-to-Point Networks

## Slide 32: Point-to-Point OSPF Networks OSPF Point-to-Point Networks (Cont.)
To change this to a point-to-point network, use the interface configuration command ip ospf network point-to-point on all interfaces where you want to disable the DR/BDR election process.
R1(config)# interface GigabitEthernet 0/0/0
R1(config-if)# ip ospf network point-to-point
*Jun 6 00:44:05.208: %OSPF-5-ADJCHG: Process 10, Nbr 2.2.2.2 on GigabitEthernet0/0/0 from FULL to DOWN, Neighbor Down: Interface down or detached
*Jun 6 00:44:05.211: %OSPF-5-ADJCHG: Process 10, Nbr 2.2.2.2 on GigabitEthernet0/0/0 from LOADING to FULL, Loading Done
R1(config-if)# end
R1# show ip ospf interface GigabitEthernet 0/0/0
GigabitEthernet0/0/0 is up, line protocol is up
Internet Address 10.1.1.5/30, Area 0, Attached via Interface Enable
Process ID 10, Router ID 1.1.1.1, Network Type POINT_TO_POINT, Cost: 1
Topology-MTID Cost Disabled Shutdown Topology Name
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.11 - OSPF Point-to-Point Networks (Cont.)

## Slide 33: Point-to-Point OSPF Networks Loopbacks and Point-to-Point Networks
Use loopbacks to provide additional interfaces for a variety of purposes. By default, loopback interfaces are advertised as /32 host routes.
To simulate a real LAN, the loopback interface can be configured as a point-to-point network to advertise the full network.
What R2 sees when R1 advertises the loopback interface as-is:
R2# show ip route | include 10.10.1
O 10.10.1.1/32 [110/2] via 10.1.1.5, 00:03:05, GigabitEthernet0/0/0
Configuration change at R1:
R1(config-if)# interface Loopback 0
R1(config-if)# ip ospf network point-to-point
Result at R2:
R2# show ip route | include 10.10.1
O 10.10.1.0/24 [110/2] via 10.1.1.5, 00:03:05, GigabitEthernet0/0/0
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.12 - Loopbacks and Point-to-Point Networks

## Slide 34: Point-to-Point OSPF Networks Packet Tracer - Point-to-Point Single-Area OSPFv2 Configuration
In this Packet Tracer activity, you will do the following:
Explicitly configure router IDs.
Configure the network command on R1 using wildcard mask based on the subnet mask.
Configure the network command on R2 using a quad-zero wildcard mask.
Configure the ip ospf interface command on R3.
Configure passive interfaces.
Verify OSPF operation using the show ip protocols and show ip route commands.
Notes: 2 - Single-Area OSPFv2 Configuration
2.2 - Point-to-Point OSPF Networks
2.2.13 - Packet Tracer - Point-to-Point Single-Area OSPFv2 Configuration

## Slide 35: 2.3 Multiaccess OSPF Networks
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks

## Slide 36: Multiaccess OSPF Networks OPSF Network Types
Another type of network that uses OSPF is the multiaccess OSPF network. Multiaccess OSPF networks are unique in that one router controls the distribution of LSAs.
The router that is elected for this role should be determined by the network administrator through proper configuration.
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.1 - OPSF Network Types

## Slide 37: Multiaccess OSPF Networks OPSF Designated Router
In multiaccess networks, OSPF elects a DR and BDR. The DR is responsible for collecting and distributing LSAs sent and received. The DR uses the multicast IPv4 address 224.0.0.5 which is meant for all OSPF routers.
A BDR is also elected in case the DR fails. The BDR listens passively and maintains a relationship with all the routers. If the DR stops producing Hello packets, the BDR promotes itself and assumes the role of DR.
All other routers become a DROTHER (a router that is neither the DR nor the BDR). DROTHERs use the multiaccess address 224.0.0.6 (all designated routers) to send OSPF packets to the DR and BDR. Only the DR and BDR listen for 224.0.0.6.
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.2 - OPSF Designated Router

## Slide 38: Multiaccess OSPF Networks OPSF Multiaccess Reference Topology
In the multiaccess topology shown in the figure, there are three routers interconnected over a common Ethernet multiaccess network, 192.168.1.0/24.
Because the routers are connected over a common multiaccess network, OSPF has automatically elected a DR and BDR. R3 has been elected as the DR because its router ID is 3.3.3.3, which is the highest in this network. R2 is the BDR because it has the second highest router ID in the network.
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.3 - OSP Multiaccess Reference Topology

## Slide 39: Multiaccess OSPF Networks Verify OSPF Router Roles
To verify the roles of the OSPFv2 router, use the show ip ospf interface command.
The output generated by R1 confirms that the following:
R1 is not the DR or BDR, but is a DROTHER with a default priority of 1. (Line 7)
The DR is R3 with router ID 3.3.3.3 at IPv4 address 192.168.1.3, while the BDR is R2 with router ID 2.2.2.2 at IPv4 address 192.168.1.2. (Lines 8 and 9)
R1 has two adjacencies: one with the BDR and one with the DR. (Lines 20-22)
R1# show ip ospf interface GigabitEthernet 0/0/0
GigabitEthernet0/0/0 is up, line protocol is up
Internet Address 192.168.1.1/24, Area 0, Attached via Interface Enable
Process ID 10, Router ID 1.1.1.1, Network Type BROADCAST, Cost: 1
(output omitted)
Transmit Delay is 1 sec, State DROTHER, Priority 1
Designated Router (ID) 3.3.3.3, Interface address 192.168.1.3
Backup Designated router (ID) 2.2.2.2, Interface address 192.168.1.2
(output omitted)
Neighbor Count is 2, Adjacent neighbor count is 2
Adjacent with neighbor 2.2.2.2 (Backup Designated Router)
Adjacent with neighbor 3.3.3.3 (Designated Router)
Suppress hello for 0 neighbor(s)
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.4 - Verify OSPF Router Roles

## Slide 40: Multiaccess OSPF Networks Verify OSPF Router Roles (Cont.)
The output generated by R2 confirms that:
R2 is the BDR with a default priority of 1. (Line 7)
The DR is R3 with router ID 3.3.3.3 at IPv4 address 192.168.1.3, while the BDR is R2 with router ID 2.2.2.2 at IPv4 address 192.168.1.2. (Lines 8 and 9)
R2 has two adjacencies; one with a neighbor with router ID 1.1.1.1 (R1) and the other with the DR. (Lines 20-22)
R2# show ip ospf interface GigabitEthernet 0/0/0
GigabitEthernet0/0/0 is up, line protocol is up
Internet Address 192.168.1.2/24, Area 0, Attached via Interface Enable
Process ID 10, Router ID 2.2.2.2, Network Type BROADCAST, Cost: 1
(output omitted)
Transmit Delay is 1 sec, State BDR, Priority 1
Designated Router (ID) 3.3.3.3, Interface address 192.168.1.3
Backup Designated Router (ID) 2.2.2.2, Interface address 192.168.1.2
(output omitted)
Neighbor Count is 2, Adjacent neighbor count is 2
Adjacent with neighbor 1.1.1.1
Adjacent with neighbor 3.3.3.3 (Designated Router)
Suppress hello for 0 neighbor(s)
R2#
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.4 - Verify OSPF Router Roles (Cont.)

## Slide 41: Multiaccess OSPF Networks Verify OSPF Router Roles (Cont.)
The output generated by R3 confirms that:
R3 is the DR with a default priority of 1. (Line 7)
The DR is R3 with router ID 3.3.3.3 at IPv4 address 192.168.1.3, while the BDR is R2 with router ID 2.2.2.2 at IPv4 address 192.168.1.2. (Lines 8 and 9)
R3 has two adjacencies: one with a neighbor with router ID 1.1.1.1 (R1) and the other with the BDR. (Lines 20-22)
R3# show ip ospf interface GigabitEthernet 0/0/0
GigabitEthernet0/0/0 is up, line protocol is up
Internet Address 192.168.1.3/24, Area 0, Attached via Interface Enable
Process ID 10, Router ID 2.2.2.2, Network Type BROADCAST, Cost: 1
(output omitted)
Transmit Delay is 1 sec, State DR, Priority 1
Designated Router (ID) 3.3.3.3, Interface address 192.168.1.3
Backup Designated Router (ID) 2.2.2.2, Interface address 192.168.1.2
(output omitted)
Neighbor Count is 2, Adjacent neighbor count is 2
Adjacent with neighbor 1.1.1.1
Adjacent with neighbor 2.2.2.2 (Backup Designated Router)
Suppress hello for 0 neighbor(s)
R3#
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.4 - Verify OSPF Router Roles (Cont.)

## Slide 42: Multiaccess OSPF Networks Verify DR/BDR Adjacencies
To verify the OSPFv2 adjacencies, use the show ip ospf neighbor command. The state of neighbors in multiaccess networks can be as follows:
FULL/DROTHER - This is a DR or BDR router that is fully adjacent with a non-DR or BDR router. These two neighbors can exchange Hello packets, updates, queries, replies, and acknowledgments.
FULL/DR - The router is fully adjacent with the indicated DR neighbor. These two neighbors can exchange Hello packets, updates, queries, replies, and acknowledgments.
FULL/BDR - The router is fully adjacent with the indicated BDR neighbor. These two neighbors can exchange Hello packets, updates, queries, replies, and acknowledgments.
2-WAY/DROTHER - The non-DR or BDR router has a neighbor relationship with another non-DR or BDR router. These two neighbors exchange Hello packets.
The normal state for an OSPF router is usually FULL. If a router is stuck in another state, it is an indication that there are problems in forming adjacencies. The only exception to this is the 2-WAY state, which is normal in a multiaccess broadcast network.
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.5 - Verify DR/BDR Adjacencies

## Slide 43: Multiaccess OSPF Networks Verify DR/BDR Adjacencies (Cont.)
The output generated by R2 confirms that R2 has adjacencies with the following routers:
R1 with router ID 1.1.1.1 is in a Full state and R1 is neither the DR nor BDR.
R3 with router ID 3.3.3.3 is in a Full state and the role of R3 is DR.
R2# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
1.1.1.1 1 FULL/DROTHER 00:00:31 192.168.1.1 GigabitEthernet0/0/0
3.3.3.3 1 FULL/DR 00:00:34 192.168.1.3 GigabitEthernet0/0/0 R2#
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.5 - Verify DR/BDR Adjacencies (Cont.)

## Slide 44: Multiaccess OSPF Networks Default DR/BDR Election Process
The OSPF DR and BDR election is based on the following criteria, in sequential order:
The routers in the network elect the router with the highest interface priority as the DR. The router with the second highest interface priority is becomes the BDR.
  The priority can be configured to be any number between 0 – 255.
  If the interface priority value is set to 0, that interface cannot be elected as DR nor BDR.
  The default priority of multiaccess broadcast interfaces is 1.
If the interface priorities are equal, then the router with the highest router ID is elected the DR. The router with the second highest router ID is the BDR.
The election process takes place when the first router with an OSPF-enabled interface is active on the network. If all of the routers on the network have not finished booting, it is possible that a router with a lower router ID becomes the DR.
The addition of a new router does not initiate a new election process.
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.6 - Default DR/BDR Election Process

## Slide 45: Multiaccess OSPF Networks DR Failure and Recovery
After the DR is elected, it remains the DR until one of the following events occurs:
The DR fails.
The OSPF process on the DR fails or is stopped.
The multiaccess interface on the DR fails or is shutdown.
If the DR fails, the BDR is automatically promoted to DR. This is the case even if another DROTHER with a higher priority or router ID is added to the network after the initial DR/BDR election. However, after a BDR is promoted to DR, a new BDR election occurs and the DROTHER with the highest priority or router ID is elected as the new BDR.
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.7 - DR Failure and Recovery

## Slide 46: Multiaccess OSPF Networks The ip ospf priority Command
If the interface priorities are equal on all routers, the router with the highest router ID is elected the DR.
Instead of relying on the router ID, it is better to control the election by setting interface priorities. This also allows a router to be the DR in one network and a DROTHER in another.
To set the priority of an interface, use the command ip ospf priority value, where value is 0 to 255.
  A value of 0 does not become a DR or a BDR.
  A value of 1 to 255 on the interface makes it more likely that the router becomes the DR or the BDR.
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.8 - The ip ospf priority Command

## Slide 47: Multiaccess OSPF Networks Configure OSPF Priority
The example shows the commands being used to change the R1 G0/0/0 interface priority from 1 to 255 and then reset the OSPF process.
R1(config)# interface GigabitEthernet 0/0/0
R1(config-if)# ip ospf priority 255
R1(config-if)# end
R1# clear ip ospf process
Reset ALL OSPF processes? [no]: y
R1# *Jun 5 03:47:41.563: %OSPF-5-ADJCHG: Process 10, Nbr 2.2.2.2 on GigabitEthernet0/0/0 from FULL to DOWN, Neighbor Down: Interface down or detached
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.9 - Configure OSPF Priority
2.3.10 - Syntax Checker - Configure OSPF Priority

## Slide 48: Multiaccess OSPF Networks Packet Tracer - Determine the DR and BDR
In this activity, you will complete the following:
Examine DR and BDR roles and watch the roles change when there is a change in the network.
Modify the priority to control the roles and force a new election.
Verify routers are filling the desired roles
Notes: 2 - Single-Area OSPFv2 Configuration
2.3 - Multiaccess OSPF Networks 2.3.11 - Packet Tracer - Determine the DR and BDR

## Slide 49: 2.4 Modify Single-Area OSPFv2
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2

## Slide 50: Modify Single-Area OSPFv2 Cisco OSPF Cost Metric
Routing protocols use a metric to determine the best path of a packet across a network. OSPF uses cost as a metric. A lower cost indicates a better path.
The Cisco cost of an interface is inversely proportional to the bandwidth of the interface. Therefore, a higher bandwidth indicates a lower cost. The formula used to calculate the OSPF cost is:
Cost = reference bandwidth / interface bandwidth
The default reference bandwidth is 108 (100,000,000); therefore, the formula is:
Cost = 100,000,000 bps / interface bandwidth in bps
Because the OSPF cost value must be an integer, FastEthernet, Gigabit Ethernet, and 10 GigE interfaces share the same cost. To correct this situation, you can:
  Adjust the reference bandwidth with the auto-cost reference-bandwidth command on each OSPF router.
  Manually set the OSPF cost value with the ip ospf cost command on necessary interfaces.
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.1 - Cisco OSPF Cost Metric

## Slide 51: Modify Single-Area OSPFv2 Cisco OSPF Cost Metric (Cont.)
Refer to the table for a breakdown of the cost calculation
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.1 - Cisco OSPF Cost Metric (Cont.)

## Slide 52: Modify Single-Area OSPFv2 Adjust the Reference Bandwidth
The cost value must be an integer. If something less than an integer is calculated, OSPF rounds up to the nearest integer. Therefore, the OSPF cost assigned to a Gigabit Ethernet interface with the default reference bandwidth of 100,000,000 bps would equal 1, because the nearest integer for 0.1 is 0 instead of 1.
Cost = 100,000,000 bps / 1,000,000,000 = 1
For this reason, all interfaces faster than Fast Ethernet will have the same cost value of 1 as a Fast Ethernet interface.
To assist OSPF in making the correct path determination, the reference bandwidth must be changed to a higher value to accommodate networks with links faster than 100 Mbps.
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.2 - Adjust the Reference Bandwidth

## Slide 53: Modify Single-Area OSPFv2 Adjust the Reference Bandwidth (Cont.)
Changing the reference bandwidth does not actually affect the bandwidth capacity on the link; rather, it simply affects the calculation used to determine the metric.
To adjust the reference bandwidth, use the auto-cost reference-bandwidth Mbps router configuration command.
  This command must be configured on every router in the OSPF domain.
  Notice in the command that the value is expressed in Mbps; therefore, to adjust the costs for Gigabit Ethernet, use the command auto-cost reference-bandwidth 1000. For 10 Gigabit Ethernet, use the command auto-cost reference-bandwidth 10000.
  To return to the default reference bandwidth, use the auto-cost reference-bandwidth 100 command.
Another option is to change the cost on one specific interface using the ip ospf cost cost command.
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.2 - Adjust the Reference Bandwidth (Cont.)

## Slide 54: Modify Single-Area OSPFv2 Adjust the Reference Bandwidth (Cont.)
Whichever method is used, it is important to apply the configuration to all routers in the OSPF routing domain.
The table shows the OSPF cost if the reference bandwidth is adjusted to accommodate 10 Gigabit Ethernet links. The reference bandwidth should be adjusted anytime there are links faster than FastEthernet (100 Mbps).
Use the show ip ospf interface command to verify the current OSPFv2 cost assigned to the interface.
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.2 - Adjust the Reference Bandwidth (Cont.)

## Slide 55: Modify Single-Area OSPFv2 OSPF Accumulates Cost
The cost of an OSPF route is the accumulated value from one router to the destination network.
Assuming the auto-cost reference-bandwidth 10000 command has been configured on all three routers, the cost of the links between each router is now 10. The loopback interfaces have a default cost of 1.
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.3 - OSPF Accumulates Cost

## Slide 56: Modify Single-Area OSPFv2 OSPF Accumulates Cost (Cont.)
You can calculate the cost for each router to reach each network.
For example, the total cost for R1 to reach the 10.10.2.0/24 network is 11. This is because the link to R2 cost = 10 and the loopback default cost = 1. 10 + 1 = 11.
You can verify this with the show ip route command.
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.3 - OSPF Accumulates Cost (Cont.)

## Slide 57: Modify Single-Area OSPFv2 OSPF Accumulates Cost (Cont.)
Verifying the accumulated cost for the path to the 10.10.2.0/24 network:
R1# show ip route | include 10.10.2.0
O 10.10.2.0/24 [110/11] via 10.1.1.6, 01:05:02, GigabitEthernet0/0/0
R1# show ip route 10.10.2.0
Routing entry for 10.10.2.0/24
Known via "ospf 10", distance 110, metric 11, type intra area
Last update from 10.1.1.6 on GigabitEthernet0/0/0, 01:05:13 ago
Routing Descriptor Blocks:
* 10.1.1.6, from 2.2.2.2, 01:05:13 ago, via GigabitEthernet0/0/0
Route metric is 11, traffic share count is 1
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.3 - OSPF Accumulates Cost (Cont.)

## Slide 58: Modify Single-Area OSPFv2 Manually Set OSPF Cost Value
Reasons to manually set the cost value include:
  The Administrator may want to influence path selection within OSPF, causing different paths to be selected than what normally would given default costs and cost accumulation.
  Connections to equipment from other vendors who use a different formula to calculate OSPF cost.
To change the cost value reported by the local OSPF router to other OSPF routers, use the interface configuration command ip ospf cost value.
R1(config)# interface g0/0/1 R1(config-if)# ip ospf cost 30 R1(config-if)# interface lo0 R1(config-if)# ip ospf cost 10 R1(config-if)# end
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.4 - Manually Set OSPF Cost Value

## Slide 59: Modify Single-Area OSPFv2 Test Failover to Backup Route
What happens if the link between R1 and R2 goes down? You can simulate that by shutting down the Gigabit Ethernet 0/0/0 interface and verifying the routing table is updated to use R3 as the next-hop router. Notice that R1 can now reach the 10.1.1.4/30 network through R3 with a cost value of 50.
R1# show ip route ospf | begin 10
10.0.0.0/8 is variably subnetted, 8 subnets, 3 masks
O 10.1.1.4/30 [110/50] via 10.1.1.13, 00:00:14, GigabitEthernet0/0/1
O 10.1.1.8/30 [110/40] via 10.1.1.13, 00:00:14, GigabitEthernet0/0/1
O 10.10.2.0/24 [110/50] via 10.1.1.13, 00:00:14, GigabitEthernet0/0/1
O 10.10.3.0/24 [110/40] via 10.1.1.13, 00:00:14, GigabitEthernet0/0/1
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.5 - Test Failover to Backup Route
2.4.6 - Syntax Checker - Modify the Cost Values for R2 and R3

## Slide 60: Modify Single-Area OSPFv2 Hello Packet Intervals
OSPFv2 Hello packets are transmitted to multicast address 224.0.0.5 (all OSPF routers) every 10 seconds. This is the default timer value on multiaccess and point-to-point networks.
  Note: Hello packets are not sent on interfaces set to passive by the passive-interface command.
The Dead interval is the period that the router waits to receive a Hello packet before declaring the neighbor down. If the Dead interval expires before the routers receive a Hello packet, OSPF removes that neighbor from its link-state database (LSDB). The router floods the LSDB with information about the down neighbor out all OSPF-enabled interfaces. Cisco uses a default of 4 times the Hello interval. This is 40 seconds on multiaccess and point-to-point networks.
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.7 - Hello Packet Intervals

## Slide 61: Modify Single-Area OSPFv2 Verify Hello and Dead Intervals
The OSPF Hello and Dead intervals are configurable on a per-interface basis.
The OSPF intervals must match or a neighbor adjacency does not occur.
To verify the currently configured OSPFv2 interface intervals, use the show ip ospf interface command. The Gigabit Ethernet 0/0/0 Hello and Dead intervals are set to the default 10 seconds and 40 seconds respectively.
R1# show ip ospf interface g0/0/0
GigabitEthernet0/0/0 is up, line protocol is up
Internet Address 10.1.1.5/30, Area 0, Attached via Interface Enable
Process ID 10, Router ID 1.1.1.1, Network Type POINT_TO_POINT, Cost: 10
Topology-MTID Cost Disabled Shutdown Topology Name
0 10 no no Base
Enabled by interface config, including secondary ip addresses
Transmit Delay is 1 sec, State POINT_TO_POINT
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
oob-resync timeout 40
(output omitted)
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.8 - Verify Hello and Dead Intervals

## Slide 62: Modify Single-Area OSPFv2 Verify Hello and Dead Intervals (Cont.)
Use the show ip ospf neighbor command to see the Dead Time counting down from 40 seconds. By default, this value is refreshed every 10 seconds when R1 receives a Hello from the neighbor.
R1# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
3.3.3.3 0 FULL/ - 00:00:35 10.1.1.13 GigabitEthernet0/0/1
2.2.2.2 0 FULL/ - 00:00:31 10.1.1.6 GigabitEthernet0/0/0
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.8 - Verify Hello and Dead Intervals (Cont.)

## Slide 63: Modify Single-Area OSPFv2 Modify OSPFv2 Intervals
It may be desirable to change the OSPF timers so that routers detect network failures in less time. Doing this increases traffic, but sometimes the need for quick convergence is more important than the extra traffic it creates.
  Note: The default Hello and Dead intervals are based on best practices and should only be altered in rare situations.
OSPFv2 Hello and Dead intervals can be modified manually using the following interface configuration mode commands:
Router(config-if)# ip ospf hello-interval seconds
Router(config-if)# ip ospf dead-interval seconds
Use the no ip ospf hello-interval and no ip ospf dead-interval commands to reset the intervals to their default.
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.9 - Modify OSPFv2 Intervals

## Slide 64: Modify Single-Area OSPFv2 Modify OSPFv2 Intervals (Cont.)
In the example, the Hello interval for the link between R1 and R2 is changed to 5 seconds. The Cisco IOS automatically modifies the Dead interval to four times the Hello interval. However, you can document the new Dead interval in the configuration by manually setting it to 20 seconds, as shown.
When the Dead Timer on R1 expires, R1 and R2 lose adjacency. R1 and R2 must be configured with the same Hello interval. Use the show ip ospf neighbor command on R1 to verify the neighbor adjacencies.
R1(config)# interface g0/0/0
R1(config-if)# ip ospf hello-interval 5
R1(config-if)# ip ospf dead-interval 20
R1(config-if)#
*Jun 7 04:56:07.571: %OSPF-5-ADJCHG: Process 10, Nbr 2.2.2.2 on GigabitEthernet0/0/0 from FULL to DOWN, Neighbor Down: Dead timer expired
R1(config-if)# end
R1# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
3.3.3.3 0 FULL/ - 00:00:37 10.1.1.13 GigabitEthernet0/0/1
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.9 - Modify OSPFv2 Intervals (Cont.)
2.4.10 - Syntax Checker - Modifying Hello and Dead Intervals on R3

## Slide 65: Modify Single-Area OSPFv2 Packet Tracer - Modify Single-Area OSPFv2
In this Packet Tracer activity, you will complete the following:
Adjust the reference bandwidth to account for gigabit and faster speeds
Modify the OSPF cost value
Modify the OSPF Hello timers
Verify the modifications are accurately reflected in the routers.
Notes: 2 - Single-Area OSPFv2 Configuration
2.4 - Modify Single-Area OSPFv2
2.4.11 - Packet Tracer - Modify Single-Area OSPFv2

## Slide 66: 2.5 Default Route Propagation
Notes: 2 - Single-Area OSPFv2 Configuration
2.5 - Default Route Propagation

## Slide 67: Default Route Propagation Propagate a Default Static Route in OSPFv2
To propagate a default route, the edge router must be configured with the following:
A default static route using the ip route 0.0.0.0 0.0.0.0 [next-hop-address | exit-intf] command.
The default-information originate router configuration command. This instructs R2 to be the source of the default route information and propagate the default static route in OSPF updates.
In the example, R2 is configured with a loopback to simulate a connection to the internet. A default route is configured and propagated to all other OSPF routers in the routing domain.
  Note: When configuring static routes, best practice is to use the next-hop IP address. However, when simulating a connection to the internet, there is no next-hop IP address. Therefore, we use the exit-intf argument.
R2(config)# interface lo1
R2(config-if)# ip address 64.100.0.1 255.255.255.252
R2(config-if)# exit
R2(config)# ip route 0.0.0.0 0.0.0.0 loopback 1
%Default route without gateway, if not a point-to-point interface, may impact performance
R2(config)# router ospf 10
R2(config-router)# default-information originate
R2(config-router)# end
R2#
Notes: 2 - Single-Area OSPFv2 Configuration
2.5 - Default Route Propagation
2.5.1 - Propagate a Default Static Route in OSPFv2

## Slide 68: Default Route Propagation Verify the Propagated Default Route
You can verify the default route settings on R2 using the show ip route command. You can also verify that R1 and R3 received a default route.
Notice that the route source on R1 is O*E2, signifying that it was learned using OSPFv2. The asterisk identifies this as a good candidate for the default route. The E2 designation identifies that it is an external route. The meaning of E1 and E2 is beyond the scope of this module.
R2# show ip route | begin Gateway
Gateway of last resort is 0.0.0.0 to network 0.0.0.0
S* 0.0.0.0/0 is directly connected, Loopback1
10.0.0.0/8 is variably subnetted, 9 subnets, 3 masks
(output omitted)
R1# show ip route | begin Gateway
Gateway of last resort is 10.1.1.6 to network 0.0.0.0
O*E2 0.0.0.0/0 [110/1] via 10.1.1.6, 00:11:08, GigabitEthernet0/0/0
10.0.0.0/8 is variably subnetted, 9 subnets, 3 masks
(output omitted)
Notes: 2 - Single-Area OSPFv2 Configuration
2.5 - Default Route Propagation
2.5.2 - Verify the Propagated Default Route

## Slide 69: Default Route Propagation Packet Tracer - Propagate a Default Route in OSPFv2
In this Packet Tracer activity, you will complete the following:
Propagate a Default Route
Part 2: Verify Connectivity
Notes: 2 - Single-Area OSPFv2 Configuration
2.5 - Default Route Propagation
2.5.3 - Packet Tracer - Propagate a Default Route in OSPFv2

## Slide 70: 2.6 Verify Single-Area OSPFv2
Notes: 2 - Single-Area OSPFv2 Configuration
2.6 - Verify Single-Area OSPFv2

## Slide 71: Verify Single-Area OSPFv2 Verify OSPF Neighbors
After configuring single-area OSPFv2, you will need to verify your configurations. The following two commands are particularly useful for verifying routing:
show ip interface brief - This verifies that the desired interfaces are active with correct IP addressing.
show ip route- This verifies that the routing table contains all the expected routes.
Additional commands for determining that OSPF is operating as expected include the following:
  show ip ospf neighbor
  show ip protocols
  show ip ospf
  show ip ospf interface
Notes: 2 - Single-Area OSPFv2 Configuration
2.6 - Verify Single-Area OSPFv2
2.6.1 - Verify OSPF Neighbors

## Slide 72: Verify Single-Area OSPFv2 Verify OSPF Neighbors (Cont.)
Use the show ip ospf neighbor command to verify that the router has formed an adjacency with its neighboring routers. If the router ID of the neighboring router is not displayed, or if it does not show as being in a state of FULL, the two routers have not formed an OSPFv2 adjacency.
  Note: A non-DR or BDR router that has a neighbor relationship with another non-DR or BDR router will display a two-way adjacency instead of full.
The following command output displays the neighbor table of R1.
R1# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
3.3.3.3 0 FULL/ - 00:00:35 10.1.1.13 GigabitEthernet0/0/1
2.2.2.2 0 FULL/ - 00:00:31 10.1.1.6 GigabitEthernet0/0/0
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.6 - Verify Single-Area OSPFv2
2.6.1 - Verify OSPF Neighbors (Cont.)

## Slide 73: Verify Single-Area OSPFv2 Verify OSPF Neighbors (Cont.)
Two routers may not form an OSPFv2 adjacency if the following occurs:
The subnet masks do not match, causing the routers to be on separate networks.
The OSPFv2 Hello or Dead Timers do not match.
The OSPFv2 Network Types do not match.
There is a missing or incorrect OSPFv2 network command.
Notes: 2 - Single-Area OSPFv2 Configuration
2.6 - Verify Single-Area OSPFv2
2.6.1 - Verify OSPF Neighbors (Cont.)

## Slide 74: Verify Single-Area OSPFv2 Verify OSPF Protocol Settings
The show ip protocols command is a quick way to verify vital OSPF configuration information, as shown in the command output. This includes the OSPFv2 process ID, the router ID, interfaces explicitly configured to advertise OSPF routes, the neighbors the router is receiving updates from, and the default administrative distance, which is 110 for OSPF.
R1# show ip protocols
*** IP Routing is NSF aware ***
(output omitted)
Routing Protocol is "ospf 10"
Outgoing update filter list for all interfaces is not set
Incoming update filter list for all interfaces is not set
Router ID 1.1.1.1
Number of areas in this router is 1. 1 normal 0 stub 0 nssa
Maximum path: 4
Routing for Networks:
Routing on Interfaces Configured Explicitly (Area 0):
Loopback0
GigabitEthernet0/0/1
GigabitEthernet0/0/0
Routing Information Sources:
Gateway Distance Last Update
3.3.3.3 110 00:09:30
2.2.2.2 110 00:09:58
Distance: (default is 110)
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.6 - Verify Single-Area OSPFv2
2.6.2 - Verify OSPF Settings

## Slide 75: Verify Single-Area OSPFv2 Verify OSPF Process Information
The show ip ospf command can also be used to examine the OSPFv2 process ID and router ID, as shown in the command output. This command displays the OSPFv2 area information and the last time the SPF algorithm was executed.
R1# show ip ospf
Routing Process "ospf 10" with ID 1.1.1.1
Start time: 00:01:47.390, Time elapsed: 00:12:32.320
(output omitted)
Cisco NSF helper support enabled
Reference bandwidth unit is 10000 mbps
Area BACKBONE(0)
Number of interfaces in this area is 3
Area has no authentication
SPF algorithm last executed 00:11:31.231 ago
SPF algorithm executed 4 times
Area ranges are
Number of LSA 3. Checksum Sum 0x00E77E
Number of opaque link LSA 0. Checksum Sum 0x000000
Number of DCbitless LSA 0 Number of indication LSA 0
Number of DoNotAge LSA 0 Flood list length 0
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.6 - Verify Single-Area OSPFv2
2.6.3 - Verify OSPF Process Information

## Slide 76: Verify Single-Area OSPFv2 Verify OSPF Interface Settings
The show ip ospf interface command provides a detailed list for every OSPFv2-enabled interface. Specify an interface to display the settings of just that interface. This command shows the process ID, the local router ID, the type of network, OSPF cost, DR and BDR information on multiaccess links (not shown), and adjacent neighbors.
R1# show ip ospf interface GigabitEthernet 0/0/0
GigabitEthernet0/0/0 is up, line protocol is up
Internet Address 10.1.1.5/30, Area 0, Attached via Interface Enable
Process ID 10, Router ID 1.1.1.1, Network Type POINT_TO_POINT, Cost: 10
<output omitted>
Neighbor Count is 1, Adjacent neighbor count is 1
Adjacent with neighbor 2.2.2.2
Suppress hello for 0 neighbor(s)
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.6 - Verify Single-Area OSPFv2
2.6.4 - Verify OSPF Interface Settings

## Slide 77: Verify Single-Area OSPFv2 Verify OSPF Interface Settings (Cont.)
To get a quick summary of OSPFv2-enabled interfaces, use the show ip ospf interface brief command, as shown in the command output. This command is useful for seeing important information including:
  Interfaces are participating in OSPF
  Networks that are being advertised (IP Address/Mask)
  Cost of each link
  Network state
  Number of neighbors on each link
R1# show ip ospf interface brief
Interface PID Area IP Address/Mask Cost State Nbrs F/C
Lo0 10 0 10.10.1.1/24 10 P2P 0/0
Gi0/0/1 10 0 10.1.1.14/30 30 P2P 1/1
Gi0/0/0 10 0 10.1.1.5/30 10 P2P 1/1
R1#
Notes: 2 - Single-Area OSPFv2 Configuration
2.6 - Verify Single-Area OSPFv2
2.6.4 - Verify OSPF Interface Settings (Cont.)
2.6.5 - Syntax Checker - Verify Single-Area OSPFv2

## Slide 78: Verify Single-Area OSPFv2 Packet Tracer - Verify Single-Area OSPFv2
In this Packet Tracer activity, you will complete the following:
Identify and verify the status of OSPF neighbors.
Determine how the routes are being learned in the network.
Explain how the neighbor state is determined.
Examine the settings for the OSPF process ID.
Add a new LAN into an existing OSPF network and verify connectivity.
Notes: 2 - Single-Area OSPFv2 Configuration
2.6 - Verify Single-Area OSPFv2
2.6.6 - Packet Tracer - Verify Single-Area OSPFv2

## Slide 79: 2.7 Module Practice and Quiz
Notes: 2 - Single-Area OSPFv2 Configuration
2.7 - Modulation Practice and Quiz

## Slide 80: Module Practice and Quiz Packet Tracer - Single-Area OSPFv2 Configuration
In this Packet Tracer activity, you will complete the following:
Implement single-area OSPFv2 in both point-to-point and broadcast multiaccess networks.
Notes: 2 - Single-Area OSPFv2 Configuration
2.7 - Modulation Practice and Quiz
2.7.1 - Packet Tracer - Single-Area OSPFv2 Configuration

## Slide 81: Module Practice and Quiz Packet Tracer – Single-Area OSPFv2 Configuration – Physical Mode Lab - Single-Area OSPFv2 Configuration
In this lab and Packet Tracer Physical Mode activity, you will complete the following objectives:
Build the network and configure basic device settings
Configure and verify single-area OSPFv2 for basic operation
Optimize and verify the single-area OSPFv2 configuration
Notes: 2 - Single-Area OSPFv2 Configuration
2.7 - Modulation Practice and Quiz
2.7.2 - Lab - Single-Area OSPFv2 Configuration

## Slide 82: Module Practice and Quiz Packet Tracer – Multiarea OSPF Configuration– Physical Mode
In this Packet Tracer Physical Mode activity, you will complete the following objectives:
Part 1: Evaluate Network Operation of Single-Area OSPF.
Part 2: Evaluate Network Operation of Multiarea OSPF.
Part 3: Configure a New Area and Attach to Area 0 Through the Internet.
Notes: 2 - Single-Area OSPFv2 Configuration
2.7 - Modulation Practice and Quiz
2.7.3 – PTPM- Multiarea OSPF Configuration

## Slide 83: Module Practice and Quiz What Did I Learn In This Module?
OSPFv2 is enabled using the router ospf process-id global configuration mode command. The process-id value represents a number between 1 and 65,535 and is selected by the network administrator.
An OSPF router ID is a 32-bit value, represented as an IPv4 address. The router ID is used by an OSPF-enabled router to synchronize OSPF databases and participate in the election of the DR and BDR.
Cisco routers derive the router ID based on one of three criteria, in this order: 1) Router ID is explicitly configured using the OSPF router-id rid router configuration mode command, 2) the router chooses the highest IPv4 address of any of configured loopback interfaces or 3) the router chooses the highest active IPv4 address of any of its physical interfaces.
The basic syntax for the network command is network network-address wildcard-mask area area-id. Any interfaces on a router that match the network address in the network command can send and receive OSPF packets.
When configuring single-area OSPFv2, the network command must be configured with the same area-id value on all routers. The wildcard mask is typically the inverse of the subnet mask configured on that interface, but could also be a quad zero wildcard mask, which would specify the exact interface.
Notes: 2 - Single-Area OSPFv2 Configuration
2.7 - Modulation Practice and Quiz
2.7.4 - What Did I Learn In This Module?

## Slide 84: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
To configure OSPF directly on the interface, use the ip ospf interface configuration mode command. The syntax is ip ospf process-id area area-id.
Use the passive-interface router configuration mode command to stop transmitting routing messages through a router interface, but still allow that network to be advertised to other routers.
The DR/ BDR election process is unnecessary as there can only be two routers on the point-to-point network between R1 and R2. Use the interface configuration command ip ospf network point-to-point on all interfaces where you want to disable the DR/BDR election process.
By default, loopback interfaces are advertised as /32 host routes. To simulate a real LAN, the Loopback 0 interface is configured as a point-to-point network.
OSPF Network Types
The DR is responsible for collecting and distributing LSAs . The DR uses the multicast IPv4 address 224.0.0.5 which is meant for all OSPF routers. If the DR stops producing Hello packets, the BDR promotes itself and assumes the role of DR. All other routers become a DROTHER.
DROTHERs use the multiaccess address 224.0.0.6 (all designated routers) to send OSPF packets to the DR and BDR. Only the DR and BDR listen for 224.0.0.6.
To verify the roles of the OSPFv2 router, use the show ip ospf interface command.
Notes: 2 - Single-Area OSPFv2 Configuration
2.7 - Modulation Practice and Quiz
2.7.4 - What Did I Learn In This Module?
(Cont.)

## Slide 85: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
To verify the OSPFv2 adjacencies, use the show ip ospf neighbor command. The state of neighbors in multiaccess networks can be: FULL/DROTHER, FULL/DR. FULL/BDR, or 2-WAY/DROTHER.
The OSPF DR and BDR election decision is based on the router with the highest interface priority as the DR. The router with the second highest interface priority is elected as the BDR. If the interface priorities are equal, then the router with the highest router ID is elected the DR. The router with the second highest router ID is the BDR.
The interface priority can be configured to be any number between 0 – 255. If the interface priority value is set to 0, that interface cannot be elected as DR nor BDR. The default priority of multiaccess broadcast interfaces is 1.
OSPF DR and BDR elections are not pre-emptive. If the DR fails, the BDR is automatically promoted to DR.
To set the priority of an interface, use the command ip ospf priority value, where value is 0 to 255. If the value is 0, the router will not become a DR or BDR. If the value is 1 to 255, then the router with the higher priority value will more likely become the DR or BDR on the interface.
OSPF uses cost as a metric. A lower cost indicates a better path than a higher cost.
The formula used to calculate the OSPF cost is: Cost = reference bandwidth / interface bandwidth.
Notes: 2 - Single-Area OSPFv2 Configuration
2.7 - Modulation Practice and Quiz
2.7.4 - What Did I Learn In This Module?
(Cont.)

## Slide 86: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
Because the OSPF cost value must be an integer, FastEthernet, Gigabit Ethernet, and 10 GigE interfaces share the same cost. To correct this situation, you can adjust the reference bandwidth with the auto-cost reference-bandwidth command on each OSPF router, or manually set the OSPF cost value with the ip ospf cost command.
The cost of an OSPF route is the accumulated value from one router to the destination network. OSPF cost values can be manipulated to influence the route chosen by OSPF. To change the cost value report by the local OSPF router to other OSPF routers, use the interface configuration command ip ospf cost value.
If the Dead interval expires before the routers receive a Hello packet, OSPF removes that neighbor from its link-state database (LSDB). The router floods the LSDB with information about the down neighbor out all OSPF-enabled interfaces.
Cisco uses a default of 4 times the Hello interval or 40 seconds on multiaccess and point-to-point networks. To verify the OSPFv2 interface intervals, use the show ip ospf interface command.
OSPFv2 Hello and Dead intervals can be modified manually using the following interface configuration mode commands: ip ospf hello-interval and ip ospf dead-interval.
Notes: 2 - Single-Area OSPFv2 Configuration
2.7 - Modulation Practice and Quiz
2.7.4 - What Did I Learn In This Module?
(Cont.)

## Slide 87: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
In OSPF terminology, the router located between an OSPF routing domain and a non-OSPF network is called the ASBR. To propagate a default route, the ASBR must be configured with a default static route using the ip route 0.0.0.0 0.0.0.0 [next-hop-address | exit-intf] command, and the default-information originate router configuration command.
Verify the default route settings on the ASBR using the show ip route command.
Additional commands for determining that OSPF is operating as expected include: show ip ospf neighbor, show ip protocols, show ip ospf, and show ip ospf interface.
Use the show ip ospf neighbor command to verify that the router has formed an adjacency with its neighboring routers.
Notes: 2 - Single-Area OSPFv2 Configuration
2.7 - Modulation Practice and Quiz
2.7.3 - What Did I Learn In This Module? (Cont.)
2.7.5 - Module Quiz - Single-Area OSPFv2 Configuration

## Slide 88: Module 2: Single-Area OSPFv2 Configuration New Terms and Commands
router ospf process-id
router ID
router-id rid
show ip protocols
show ip ospf
network network-address wildcard-mask area area-id
ip ospf process-id area area-id
passive interface
passive-interface intf-id
show ip ospf interface intf-id
ip ospf network point-to-point
host route
designated router (DR)
backup designated router (BDR)
DROTHER
show ip ospf neighbor
ip ospf priority
clear ip ospf process
metric
cost
auto-cost reference-bandwidth Mbps
ip ospf cost value
ip ospf hello-interval value
ip ospf dead-interval value
default-information originate