## Slide 1: Module 4: ACL Concepts
Instructor Materials
Enterprise Networking, Security, and Automationv7.0
(ENSA)
Notes: Cisco Networking Academy Program
Enterprise Networking, Security, and Automationv7.0 (ENSA)
Module 4: ACL Concepts

## Slide 2: Instructor Materials – Module 4 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the module
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 9
  Note: Remove the Planning Guide from this presentation before sharing with anyone.
For additional help and resources go to the Instructor Home Page and Course Resources for this course. You also can visit the professional development site on netacad.com, the official Cisco Networking Academy Facebook page, or Instructor Only FB group.
Notes: 2

## Slide 3: What to Expect in this Module
To facilitate learning, the following features within the GUI may be included in this module:
Feature | Description
Animations | Expose learners to new skills and concepts.
Videos | Expose learners to new skills and concepts.
Check Your Understanding(CYU) | Per topic online quiz to help learners gauge content understanding.
Interactive Activities | A variety of formats to help learners gauge content understanding.
Syntax Checker | Small simulations that expose learners to Cisco command line to practice configuration skills.
PT Activity | Simulation and modeling activities designed to explore, acquire, reinforce, and expand skills.

## Slide 4: What to Expect in this Module (Cont.)
To facilitate learning, the following features may be included in this module:
Feature | Description
Hands-On Labs | Labs designed for working with physical equipment.
Class Activities | These are found on the Instructor Resources page. Class Activities are designed to facilitate learning, class discussion, and collaboration.
Module Quizzes | Self-assessments that integrate concepts and skills learned throughout the series of topics presented in the module.
Module Summary | Briefly recaps module content.

## Slide 5: Check Your Understanding
Check Your Understanding activities are designed to let students quickly determine if they understand the content and can proceed, or if they need to review.
Check Your Understanding activities do not affect student grades.
There are no separate slides for these activities in the PPT. They are listed in the notes area of the slide that appears before these activities.
Notes: 5

## Slide 6: Module 4: Activities
What activities are associated with this module?
Page # | Activity Type | Activity Name | Optional?
4.1.4 | Packet Tracer | ALC Demonstration | Recommended
4.1.5 | Check Your Understanding | Purpose of ACLs | Recommended
4.2.5 | Check Your Understanding | Wildcard Masks in ACLs | Recommended
4.3.3 | Check Your Understanding | Guidelines for ACL Creation | Recommended
4.4.6 | Check Your Understanding | Guidelines for ACL Placement | Recommended
4.5.2 | Module Quiz | ACL Concepts | Recommended
Notes: 6

## Slide 7: Module 4: Best Practices
Prior to teaching Module 4, the instructor should:
Review the activities and assessments for this module.
Try to include as many questions as possible to keep students engaged during classroom presentation.
Topic 4.1
  Ask the students or have a class discussion
    Discuss and clarify what inbound and outbound mean with regard to ACLs.
    What system or mechanism might provide filtering above Layer 4?
Topic 4.2
  Ask the students or have a class discussion
    Create several exercises to reinforce how wildcard masks are calculated for ranges of networks.
    What is the main benefit derived from the host and any keywords?
Notes: 7

## Slide 8: Module 4: Best Practices (Cont.)
Topic 4.3
  Ask the students or have a class discussion
    Why is writing an ACL out in a text editor considered a best practice?
    What are the different ways that an ACL might be documented?
Topic 4.4
  Ask the students or have a class discussion
    What is the main concept behind the guidelines for where to place ACLs?
    Create several exercises to reinforce ACL placement guidelines.
Notes: 8

## Slide 9: Module 4: ACL Concepts
Enterprise Networking, Security, and Automation v7.0
(ENSA)
Notes: Cisco Networking Academy Program
Enterprise Networking, Security, and Automationv7.0 (ENSA)
Module 4: ACL Concepts

## Slide 10: Module Objectives
Module Title: ACL Concepts
Module Objective: Explain how ACLs are used as part of a network security policy.
Topic Title | Topic Objective
Purpose of ACLs | Explain how ACLs filter traffic.
Wildcard Masks in ACLs | Explain how ACLs use wildcard masks.
Guidelines for ACL Creation | Explain how to create ACLs.
Types of IPv4 ACLs | Compare standard and extended IPv4 ACLs.
Notes: 10

## Slide 11: 4.1 Purpose of ACLs
Notes: 4 - ACL Concepts
4.1 - Purpose of ACLs

## Slide 12: Purpose of ACLs What is an ACL?
An ACL is a series of IOS commands that are used to filter packets based on information found in the packet header. By default, a router does not have any ACLs configured. When an ACL is applied to an interface, the router performs the additional task of evaluating all network packets as they pass through the interface to determine if the packet can be forwarded.
An ACL uses a sequential list of permit or deny statements, known as access control entries (ACEs).
Note: ACEs are also commonly called ACL statements.
When network traffic passes through an interface configured with an ACL, the router compares the information within the packet against each ACE, in sequential order, to determine if the packet matches one of the ACEs. This process is called packet filtering.
Notes: 4 - ACL Concepts
4.1 - Purpose of ACLs
4.1.1 - What is an ACL?

## Slide 13: Purpose of ACLs What is an ACL? (Cont.)
Several tasks performed by routers require the use of ACLs to identify traffic:
Limit network traffic to increase network performance
Provide traffic flow control
Provide a basic level of security for network access
Filter traffic based on traffic type
Screen hosts to permit or deny access to network services
Provide priority to certain classes of network traffic
Notes: 4 - ACL Concepts
4.1 - Purpose of ACLs
4.1.1 - What is an ACL? (Cont.)

## Slide 14: Purpose of ACLs Packet Filtering
Packet filtering controls access to a network by analyzing the incoming and/or outgoing packets and forwarding them or discarding them based on given criteria.
Packet filtering can occur at Layer 3 or Layer 4.
Cisco routers support two types of ACLs:
  Standard ACLs - ACLs only filter at Layer 3 using the source IPv4 address only.
  Extended ACLs - ACLs filter at Layer 3 using the source and / or destination IPv4 address. They can also filter at Layer 4 using TCP, UDP ports, and optional protocol type information for finer control.
Notes: 4 - ACL Concepts
4.1 - Purpose of ACLs
4.1.2 - Packet Filtering

## Slide 15: Purpose of ACLs ACL Operation
ACLs define the set of rules that give added control for packets that enter inbound interfaces, packets that relay through the router, and packets that exit outbound interfaces of the router.
ACLs can be configured to apply to inbound traffic and outbound traffic.
Note: ACLs do not act on packets that originate from the router itself.
An inbound ACL filters packets before they are routed to the outbound interface. An inbound ACL is efficient because it saves the overhead of routing lookups if the packet is discarded.
An outbound ACL filters packets after being routed, regardless of the inbound interface.
Notes: 4 - ACL Concepts
4.1 - Purpose of ACLs
4.1.3 - ACL Operation

## Slide 16: Purpose of ACLs ACL Operation (Cont.)
When an ACL is applied to an interface, it follows a specific operating procedure. Here are the operational steps used when traffic has entered a router interface with an inbound standard IPv4 ACL configured:
  The router extracts the source IPv4 address from the packet header.
  The router starts at the top of the ACL and compares the source IPv4 address to each ACE in a sequential order.
  When a match is made, the router carries out the instruction, either permitting or denying the packet, and the remaining ACEs in the ACL, if any, are not analyzed.
  If the source IPv4 address does not match any ACEs in the ACL, the packet is discarded because there is an implicit deny ACE automatically applied to all ACLs.
The last ACE statement of an ACL is always an implicit deny that blocks all traffic. It is hidden and not displayed in the configuration.
  Note: An ACL must have at least one permit statement otherwise all traffic will be denied due to the implicit deny ACE statement.
Notes: 4 - ACL Concepts
4.1 - Purpose of ACLs
4.1.3 - ACL Operation (Cont.)

## Slide 17: Purpose of ACLs Packet Tracer - ACL Demonstration
In this Packet Tracer, you will complete the following objectives:
Part 1: Verify Local Connectivity and Test Access Control List
Part 2: Remove Access Control List and Repeat Test
Notes: 4 - ACL Concepts
4.1 - Purpose of ACLs
4.1.4 - Packet Tracer - ACL Demonstration
4.1.5 - Check Your Understanding - Purpose of ACLs

## Slide 18: 4.2 Wildcard Masks in ACLs
Notes: 4 - ACL Concepts
4.2 - Wildcard Masks in ACLs

## Slide 19: Wildcard Masks in ACLs Wildcard Mask Overview
A wildcard mask is similar to a subnet mask in that it uses the ANDing process to identify which bits in an IPv4 address to match. Unlike a subnet mask, in which binary 1 is equal to a match and binary 0 is not a match, in a wildcard mask, the reverse is true.
An IPv4 ACE uses a 32-bit wildcard mask to determine which bits of the address to examine for a match.
Wildcard masks use the following rules to match binary 1s and 0s:
  Wildcard mask bit 0 - Match the corresponding bit value in the address
  Wildcard mask bit 1 - Ignore the corresponding bit value in the address
Notes: 4 - ACL Concepts
4.2 - Wildcard Masks in ACLs
4.2.1 - Wildcard Mask Overview

## Slide 20: Wildcard Masks in ACLs Wildcard Mask Overview (Cont.)
Wildcard Mask | Last Octet (in Binary) | Meaning (0 - match, 1 - ignore)
0.0.0.0 | 00000000 | Match all octets.
0.0.0.63 | 00111111 | Match the first three octets Match the two left most bits of the last octet Ignore the last 6 bits
0.0.0.15 | 00001111 | Match the first three octets Match the four left most bits of the last octet Ignore the last 4 bits of the last octet
0.0.0.248 | 11111100 | Match the first three octets Ignore the six left most bits of the last octet Match the last two bits
0.0.0.255 | 11111111 | Match the first three octet Ignore the last octet
Notes: 4 - ACL Concepts
4.2 - Wildcard Masks in ACLs
4.2.1 - Wildcard Mask Overview (Cont.)

## Slide 21: Wildcard Masks in ACLs Wildcard Mask Types
Wildcard to Match a Host:
Assume ACL 10 needs an ACE that only permits the host with IPv4 address 192.168.1.1. Recall that “0” equals a match and “1” equals ignore. To match a specific host IPv4 address, a wildcard mask consisting of all zeroes (i.e., 0.0.0.0) is required.
When the ACE is processed, the wildcard mask will permit only the 192.168.1.1 address. The resulting ACE in ACL 10 would be access-list 10 permit 192.168.1.1 0.0.0.0.
 | Decimal | Binary
IPv4 address | 192.168.1.1 | 11000000.10101000.00000001.00000001
Wildcard Mask | 0.0.0.0 | 00000000.00000000.00000000.00000000
Permitted IPv4 Address | 192.168.1.1 | 11000000.10101000.00000001.00000001
Notes: 4 - ACL Concepts
4.2 - Wildcard Masks in ACLs
4.2.2 - Wildcard Mask Types

## Slide 22: Wildcard Masks in ACLs Wildcard Mask Types (Cont.)
Wildcard Mask to Match an IPv4 Subnet
ACL 10 needs an ACE that permits all hosts in the 192.168.1.0/24 network. The wildcard mask 0.0.0.255 stipulates that the very first three octets must match exactly but the fourth octet does not.
When processed, the wildcard mask 0.0.0.255 permits all hosts in the 192.168.1.0/24 network. The resulting ACE in ACL 10 would be access-list 10 permit 192.168.1.0 0.0.0.255.
 | Decimal | Binary
IPv4 address | 192.168.1.1 | 11000000.10101000.00000001.00000001
Wildcard Mask | 0.0.0.255 | 00000000.00000000.00000000.11111111
Permitted IPv4 Address | 192.168.1.0/24 | 11000000.10101000.00000001.00000000
Notes: 4 - ACL Concepts
4.2 - Wildcard Masks in ACLs
4.2.2 - Wildcard Mask Types (Cont.)

## Slide 23: Wildcard Masks in ACLs Wildcard Mask Types (Cont.)
Wildcard Mask to Match an IPv4 Address Range
ACL 10 needs an ACE that permits all hosts in the 192.168.16.0/24, 192.168.17.0/24, …, 192.168.31.0/24 networks.
When processed, the wildcard mask 0.0.15.255 permits all hosts in the 192.168.16.0/24 to 192.168.31.0/24 networks. The resulting ACE in ACL 10 would be access-list 10 permit 192.168.16.0 0.0.15.255.
 | Decimal | Binary
IPv4 address | 192.168.16.0 | 11000000.10101000.00010000.00000000
Wildcard Mask | 0.0.15.255 | 00000000.00000000.00001111.11111111
Permitted IPv4 Address | 192.168.16.0/24 to 192.168.31.0/24 | 11000000.10101000.00010000.00000000 11000000.10101000.00011111.00000000
Notes: 4 - ACL Concepts
4.2 - Wildcard Masks in ACLs
4.2.2 - Wildcard Mask Types (Cont.)

## Slide 24: Wildcard Masks in ACLs Wildcard Mask Calculation
Calculating wildcard masks can be challenging. One shortcut method is to subtract the subnet mask from 255.255.255.255. Some examples:
Assume you wanted an ACE in ACL 10 to permit access to all users in the 192.168.3.0/24 network. To calculate the wildcard mask, subtract the subnet mask (255.255.255.0) from 255.255.255.255. This produces the wildcard mask 0.0.0.255. The ACE would be access-list 10 permit 192.168.3.0 0.0.0.255.
Assume you wanted an ACE in ACL 10 to permit network access for the 14 users in the subnet 192.168.3.32/28. Subtract the subnet (i.e., 255.255.255.240) from 255.255.255.255. This produces the wildcard mask 0.0.0.15. The ACE would be access-list 10 permit 192.168.3.32 0.0.0.15.
Assume you needed an ACE in ACL 10 to permit only networks 192.168.10.0 and 192.168.11.0. These two networks could be summarized as 192.168.10.0/23 which is a subnet mask of 255.255.254.0. Subtract 255.255.254.0 subnet mask from 255.255.255.255. This produces the wildcard mask 0.0.1.255. The ACE would be access-list 10 permit 192.168.10.0 0.0.1.255.
Notes: 4 - ACL Concepts
4.2 - Wildcard Masks in ACLs
4.2.3 - Wildcard Mask Calculation

## Slide 25: Wildcard Masks in ACLs Wildcard Mask Keywords
The Cisco IOS provides two keywords to identify the most common uses of wildcard masking. The two keywords are:
host - This keyword substitutes for the 0.0.0.0 mask. This mask states that all IPv4 address bits must match to filter just one host address.
any - This keyword substitutes for the 255.255.255.255 mask. This mask says to ignore the entire IPv4 address or to accept any addresses.
Notes: 4 - ACL Concepts
4.2 - Wildcard Masks in ACLs
4.2.4 - Wildcard Mask Keywords
4.2.5 - Check Your Understanding - Wildcard Masks in ACLs

## Slide 26: 4.3 Guidelines for ACL Creation
Notes: 4 - ACL Concepts
4.3 - Guidelines for ACLs

## Slide 27: Guidelines for ACL Creation Limited Number of ACLs per Interface
There is a limit on the number of ACLs that can be applied on a router interface. For example, a dual-stacked (i.e, IPv4 and IPv6) router interface can have up to four ACLs applied, as shown in the figure.
Specifically, a router interface can have:
One outbound IPv4 ACL.
One inbound IPv4 ACL.
One inbound IPv6 ACL.
One outbound IPv6 ACL.
Note: ACLs do not have to be configured in both directions. The number of ACLs and their direction applied to the interface will depend on the security policy of the organization.
Notes: 4 - ACL Concepts
4.3 - Guidelines for ACLs
4.3.1 - Limited Number of ACLs per Interface

## Slide 28: Guidelines for ACL Creation ACL Best Practices
Using ACLs requires attention to detail and great care. Mistakes can be costly in terms of downtime, troubleshooting efforts, and poor network service. Basic planning is required before configuring an ACL.
Guideline | Benefit
Base ACLs on the organizational security policies. | This will ensure you implement organizational security guidelines.
Write out what you want the ACL to do. | This will help you avoid inadvertently creating potential access problems.
Use a text editor to create, edit, and save all of your ACLs. | This will help you create a library of reusable ACLs.
Document the ACLs using the remark command. | This will help you (and others) understand the purpose of an ACE.
Test the ACLs on a development network before implementing them on a production network. | This will help you avoid costly errors.
Notes: 4 - ACL Concepts
4.3 - Guidelines for ACLs
4.3.1 - Limited Number of ACLs per Interface
4.3.2 - Check Your Understanding - Guidelines for ACL Creation

## Slide 29: 4.4 Types of IPv4 ACLs
Notes: 4 - ACL Concepts
4.4 - Types of IPv4 ACLs

## Slide 30: Types of IPv4 ACLs Standard and Extended ACLs
There are two types of IPv4 ACLs:
Standard ACLs - These permit or deny packets based only on the source IPv4 address.
Extended ACLs - These permit or deny packets based on the source IPv4 address and destination IPv4 address, protocol type, source and destination TCP or UDP ports and more.
Notes: 4 - ACL Concepts
4.4 - Types of IPv4 ACLs
4.4.1 - Standard and Extended ACLs

## Slide 31: Types of IPv4 ACLs Numbered and Named ACLs
Numbered ACLs
ACLs numbered 1-99, or 1300-1999 are standard ACLs, while ACLs numbered 100-199, or 2000-2699 are extended ACLs.
R1(config)# access-list ?
<1-99> IP standard access list
<100-199> IP extended access list
<1100-1199> Extended 48-bit MAC address access list
<1300-1999> IP standard access list (expanded range)
<200-299> Protocol type-code access list
<2000-2699> IP extended access list (expanded range)
<700-799> 48-bit MAC address access list
rate-limit Simple rate-limit specific access list
template Enable IP template acls
Router(config)# access-list
Notes: 4 - ACL Concepts
4.4 - Types of IPv4 ACLs
4.4.2 - Numbered and Named ACLs

## Slide 32: Types of IPv4 ACLs Numbered and Named ACLs (Cont.)
Named ACLs
Named ACLs are the preferred method to use when configuring ACLs. Specifically, standard and extended ACLs can be named to provide information about the purpose of the ACL. For example, naming an extended ACL FTP-FILTER is far better than having a numbered ACL 100.
The ip access-list global configuration command is used to create a named ACL, as shown in the following example.
R1(config)# ip access-list extended FTP-FILTER
R1(config-ext-nacl)# permit tcp 192.168.10.0 0.0.0.255 any eq ftp
R1(config-ext-nacl)# permit tcp 192.168.10.0 0.0.0.255 any eq ftp-data R1(config-ext-nacl)#
Notes: 4 - ACL Concepts
4.4 - Types of IPv4 ACLs
4.4.2 - Numbered and Named ACLs (Cont.)

## Slide 33: Types of IPv4 ACLs Where to Place ACLs
Every ACL should be placed where it has the greatest impact on efficiency.
Extended ACLs should be located as close as possible to the source of the traffic to be filtered.
Standard ACLs should be located as close to the destination as possible.
Notes: 4 - ACL Concepts
4.4 - Types of IPv4 ACLs
4.4.3 - Where to Place ACLs

## Slide 34: Types of IPv4 ACLs Where to Place ACLs (Cont.)
Factors Influencing ACL Placement | Explanation
The extent of organizational control | Placement of the ACL can depend on whether or not the organization has control of both the source and destination networks.
Bandwidth of the networks involved | It may be desirable to filter unwanted traffic at the source to prevent transmission of bandwidth-consuming traffic.
Ease of configuration | It may be easier to implement an ACL at the destination, but traffic will use bandwidth unnecessarily. An extended ACL could be used on each router where the traffic originated. This would save bandwidth by filtering the traffic at the source, but it would require creating extended ACLs on multiple routers.
Notes: 4 - ACL Concepts
4.4 - Types of IPv4 ACLs
4.4.3 - Where to Place ACLs (Cont.)

## Slide 35: Types of IPv4 ACLs Standard ACL Placement Example
In the figure, the administrator wants to prevent traffic originating in the 192.168.10.0/24 network from reaching the 192.168.30.0/24 network.
Following the basic placement guidelines, the administrator would place a standard ACL on router R3.
Notes: 4 - ACL Concepts
4.4 - Types of IPv4 ACLs
4.4.4 - Standard ACL Placement Example

## Slide 36: Types of IPv4 ACLs Standard ACL Placement Example (Cont.)
There are two possible interfaces on R3 to apply the standard ACL:
R3 S0/1/1 interface (inbound) - The standard ACL can be applied inbound on the R3 S0/1/1 interface to deny traffic from .10 network. However, it would also filter .10 traffic to the 192.168.31.0/24 (.31 in this example) network. Therefore, the standard ACL should not be applied to this interface.
R3 G0/0 interface (outbound) - The standard ACL can be applied outbound on the R3 G0/0/0 interface. This will not affect other networks that are reachable by R3. Packets from .10 network will still be able to reach the .31 network. This is the best interface to place the standard ACL to meet the traffic requirements.
Notes: 4 - ACL Concepts
4.4 - Types of IPv4 ACLs
4.4.4 - Standard ACL Placement Example (Cont.)

## Slide 37: Types of IPv4 ACLs Extended ACL Placement Example
Extended ACLs should be located as close to the source as possible.
However, the organization can only place ACLs on devices that they control. Therefore, the extended ACL placement must be determined in the context of where organizational control extends.
In the figure, for example, Company A wants to deny Telnet and FTP traffic to Company B’s 192.168.30.0/24 network from their 192.168.11.0/24 network, while permitting all other traffic.
Notes: 4 - ACL Concepts
4.4 - Types of IPv4 ACLs
4.4.5 - Extended ACL Placement Example

## Slide 38: Types of IPv4 ACLs Extended ACL Placement Example (Cont.)
An extended ACL on R3 would accomplish the task, but the administrator does not control R3. In addition, this solution allows unwanted traffic to cross the entire network, only to be blocked at the destination.
The solution is to place an extended ACL on R1 that specifies both source and destination addresses.
There are two possible interfaces on R1 to apply the extended ACL:
R1 S0/1/0 interface (outbound) - The extended ACL can be applied outbound on the S0/1/0 interface. This solution will process all packets leaving R1 including packets from 192.168.10.0/24.
R1 G0/0/1 interface (inbound) - The extended ACL can be applied inbound on the G0/0/1 and only packets from the 192.168.11.0/24 network are subject to ACL processing on R1. Because the filter is to be limited to only those packets leaving the 192.168.11.0/24 network, applying the extended ACL to G0/1 is the best solution.
Notes: 4 - ACL Concepts
4.4 - Types of IPv4 ACLs
4.4.5 - Extended ACL Placement Example (Cont.)
4.4.5 - Check Your Understanding - Guidelines for ACL Placement

## Slide 39: 4.5 Module Practice and Quiz
Notes: 4 - ACL Concepts
4.5 - Module Practice and Quiz

## Slide 40: Module Practice and Quiz What Did I Learn In This Module?
An ACL is a series of IOS commands that are used to filter packets based on information found in the packet header.
A router does not have any ACLs configured by default.
When an ACL is applied to an interface, the router performs the additional task of evaluating all network packets as they pass through the interface to determine if the packet can be forwarded.
An ACL uses a sequential list of permit or deny statements, known as ACEs.
Cisco routers support two types of ACLs: standard ACLs and extended ACLs.
An inbound ACL filters packets before they are routed to the outbound interface. If the packet is permitted by the ACL, it is then processed for routing.
An outbound ACL filters packets after being routed, regardless of the inbound interface.
An IPv4 ACE uses a 32-bit wildcard mask to determine which bits of the address to examine for a match.
A wildcard mask is similar to a subnet mask in that it uses the ANDing process to identify which bits in an IPv4 address to match. However, they differ in the way they match binary 1s and 0s. Wildcard mask bit 0 matches the corresponding bit value in the address. Wildcard mask bit 1 ignores the corresponding bit value in the address.
Notes: 4 - ACL Concepts
4.5 - Module Practice and Quiz
4.5.1 - What Did I Learn In This Module?

## Slide 41: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
A shortcut to calculating a wildcard mask is to subtract the subnet mask from 255.255.255.255.
Working with decimal representations of binary wildcard mask bits can be simplified by using the Cisco IOS keywords host and any to identify the most common uses of wildcard masking.
There is a limit on the number of ACLs that can be applied on a router interface.
ACLs do not have to be configured in both directions. The number of ACLs and their direction applied to the interface will depend on the security policy of the organization.
Standard ACLs permit or deny packets based only on the source IPv4 address.
Extended ACLs permit or deny packets based on the source IPv4 address and destination IPv4 address, protocol type, source and destination TCP or UDP ports and more.
ACLs numbered 1-99, or 1300-1999, are standard ACLs. ACLs numbered 100-199, or 2000-2699, are extended ACLs.
Named ACLs is the preferred method to use when configuring ACLs.
Specifically, standard and extended ACLs can be named to provide information about the purpose of the ACL.
Every ACL should be placed where it has the greatest impact on efficiency.
Notes: 4 - ACL Concepts
4.5 - Module Practice and Quiz
4.5.1 - What Did I Learn In This Module? (Cont.)

## Slide 42: Module Practice and Quiz What Did I Learn In This Module? (Cont.)
Extended ACLs should be located as close as possible to the source of the traffic to be filtered. This way, undesirable traffic is denied close to the source network without crossing the network infrastructure.
Standard ACLs should be located as close to the destination as possible. If a standard ACL was placed at the source of the traffic, the "permit" or "deny" will occur based on the given source address no matter where the traffic is destined.
Placement of the ACL may depend on the extent of organizational control, bandwidth of the networks, and ease of configuration.
Notes: 4 - ACL Concepts
4.5 - Module Practice and Quiz
4.5.1 - What Did I Learn In This Module? (Cont.)
4.5.2 - Module Quiz - ACL Concepts

## Slide 43: Module 4 : Network Automation New Terms and Commands
access control list (ACL)
access control element (ACE)
packet filtering
standard ACLs
extended ACLs
wildcard mask
host keyword
any keyword
numbered ACLs
named ACLs